## Slide 1: CHALLENGE 5 Steering the Car
Group 3
Aoshuang wang, lan yao, yixuan huang, lan luo

## Slide 2
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
Challenge 1 | Presenter |  |  | 
Challenge 2 |  |  | Presenter | 
Challenge 3 |  | Presenter |  | 
Challenge 4 |  |  |  | Presenter
Challenge 5 | Presenter |  |  | 
Challenge 6 |  |  |  | 
Challenge 7 |  |  |  | 
Challenge 8 |  |  |  | 

## Slide 3
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
 | Program Writing (assess the situation) Configure Component Parameter | Program Writing (PID / assess the situation/html) Configure Component Parameter | Hardware Access Configure Component Parameter | IOS App Design & Control Program Writing (assess the situation) Configure Component Parameter

## Slide 4
Devices
Router
Laptop
Phone
Auto-Car
Photon

## Slide 5: Sensors
Sonic (Front)
Lidar * 1
(one side)
Speed sensor (right beside wheel)
Distance Sensor

## Slide 6: Main Architecture
Photon
Particle
ESC (speed)
Wheels (direction)
Controls
Distance/speed Sensors

## Slide 7: Data structure
if: Dist (Sonic) < 100: speed down: esc.write(90)
if: Dist (Sharp1) <70: PID Sharp1 to 50: wheels.write(90 + pid output)
(elif: Dist (Sharp2) < 70: PID Sjarp2 to 50: wheels.write(90 - pid output))

## Slide 8: Design Details
PID:
Setpoint (desired output),
Input (real data),
Output (applied data through PID)

## Slide 9: What we have done sensor
Lidar (distance sensors):
Two lidars: left and right
When Lidar1 distance < 70 (situation that lidar1 side has a gap on the wall -> PID Lidar2
When Lidar2 distance < 70 (situation that lida2 side has a gap on the wall ->PID Lidar1
Control the direction of auto car

## Slide 10: What we have done sensor
Sonic (distance sensors):
One sensor: front
When sensor distance < 100: there is an obstacle in front of the car, the car needs to stop
PID ESC to 90 (stop)
Control the stop and run

## Slide 11: What we have done html

## Slide 12: What we have done app

## Slide 13
Library:
Particle iOS Cloud SDK
Particle iOS Cloud SDK enables iOS apps to interact with Particle-powered connected products via the Particle Cloud. It’s an easy-to-use wrapper for Particle REST API.

## Slide 14
LOGGING IN TO PARTICLE CLOUD
GET A LIST OF ALL DEVICES
CHOOSE THE DEVICE TO CONNECT
CALL A FUNCTION ON A PARTICLE DEVICE
SUBSCRIBE TO EVENTS:”SPEED”
SET ‘ON’ TO RUN CRAWLER
AND
SET ‘OFF’ TO STOP CRAWLER
CHANGE SPEED OF CRAWLER
GET SPEED OF CRAWLER

## Slide 15
GET SPEED OF CRAWLER
SparkEventHandler handler = ^(SparkEvent *event, NSError *error) {
if (!error)
{
dispatch_async(dispatch_get_main_queue(), ^{
NSLog(@"Got Event %@ with data: %@",event.event,event.data);
_speed.text=event.data;
});
}
else
{
NSLog(@"Error occured: %@",error.localizedDescription);
}
};
// This line actually subscribes to the event stream:
id eventListenerID = [[SparkCloud sharedInstance] subscribeToDeviceEventsWithPrefix:@"Speed1" deviceID:@"230044001547353236343033" handler:handler];
NSLog(@"%@",eventListenerID);

## Slide 16
CODE IN PHOTON
switch (which_command) {
case 1:
esc.write(70);
// digitalWrite(aaa,HIGH);
which_command = 0;
break;
case 2:
esc.write(90);
// digitalWrite(aaa,LOW);
which_command = 0;
break;
int lightLED(String cmd) {
if(cmd == "ON") {
// digitalWrite(D7, HIGH);
which_command=1;
return 1;
}
else if(cmd == "OFF") {
// digitalWrite(D7, LOW);
which_command=2;
return 2;
}
}

## Slide 17
SET ‘ON’ , ‘OFF’ AND CHANGE SPEED OF CRAWLER
NSURLSessionDataTask *task = [myPhoton callFunction:@"fun_test" withArguments:@[@"ON"] completion:^(NSNumber *resultCode, NSError *error) {
if (!error)
{
NSLog(@“Successful!!!”);
}
else
{
NSLog(@"wrong~~");
}
}];

## Slide 18
if(value1>20 && value1<=30)
{
NSURLSessionDataTask *changespeed3 = [myPhoton callFunction:@"fun_test1" withArguments:@[@"25"] completion:^(NSNumber *resultCode, NSError *error) {
if (!error)
{
NSLog(@“Successful!!!”);
}
NSLog(@"wrong~~");
}];
}

## Slide 19
CODE IN PHOTON
int speed(String cmd){
if(cmd == "25")
{
which_command=25;
return 25;
}
switch (which_command) {
case 25:
esc.write(65);
// digitalWrite(aaa,HIGH);
which_command = 0;
break;

## Slide 20: Challenges Encountered and Resolved sensor
Sensors easy to break:
We use two lidars at the beginning and so it will continue going straight forward even though there is a gap on one side. However, one of our lidars was broken, we have to use only one lidar which would not solve the problem of gap.

## Slide 21: Challenges Encountered and Resolved sensor
Sensors accuracy:
The sensors’ accuracy needs to be improved if we want to make a right straight line traveling.

## Slide 22: Challenges Encountered and Resolved particle
Flash problem:
When we were trying to flash our improved program into photon, there always was a time-out warning. We can only flash our code into photon successfully after we have tried hundreds of times and we are pretty sure that our photon and program are correct.

## Slide 23: Challenges Encountered and Resolved HTML

## Slide 24: Challenges Encountered and Resolved app
Long Delay of Call Function
It will cost a long time for our application and photon to finish call function(run, stop, and change speed of crawler).
Data change of UISlide too fast
Data of the UISlider changes so many times when we want to change the speed of crawler from original(ex. 60) to a new one(ex. 70), so that our photon could not response in time.