## Slide 1: CHALLENGE 7 Infectious Swarm
Group 3
Aoshuang wang, lan yao, yixuan huang, lan luo

## Slide 2
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
Challenge 1 | Presenter |  |  | 
Challenge 2 |  |  | Presenter | 
Challenge 3 |  | Presenter |  | 
Challenge 4 |  |  |  | Presenter
Challenge 5 | Presenter |  |  | 
Challenge 6 |  |  | Presenter | 
Challenge 7 |  | Presenter |  | 
Challenge 8 |  |  |  | 

## Slide 3
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
 | Program Writing | Program Writing &Debugging | Hardware Connection | Program Writing &Debugging

## Slide 4
Pressing the button with either start an infection or clear an infection depending on being a leader or a non-leader .
One leader is elected on startup. A new leader is elected if an existing leader disappears.
While infected, each device will send out infection messages to other connected devices.
A clear infection message has priority over infection message.

## Slide 5
Blue : Leader
Red : Infected
Green : uninfected

## Slide 6
Election Algorithm
Bully Algorithm vs Ring Election Algorithm
For Bully Algorithm
  Worst case : initiator is with the lowest ID
  Triggers n-2 elections at higher ranked devices, n2 messages
  Best case : initiator is with the highest ID
  Immediate election, n -1 messages
For Ring Election Algorithm
  2n messages always
Bully Algorithm:
Any device can initiate an election
Device who initiates the election only sends messages to devices with higher ID
The system is synchronous and uses timeout for identifying process failure
Allows processes to crash during execution of algorithm
Prior information about other process ID’s are known

## Slide 7
For each Arduino
We tag every Arduino(XBee) with a unique ID number – serial address.
Maintain a list of addresses of XBees that it can successfully hear from.
Whenever we add a new Xbee into the network, the election system can handle it by adding the address of new Xbees to the tail of the list.

## Slide 8
For each Arduino - Messages in payload includes :
DISCOVERYMESSAGE:
Happens when a device is just set up/join the network for the first time
ACKNOWLEDGE:
Happens when my device received a message of “begin election” from other devices
ELECTIONMESSAGE:
Happens when I am the one who starts the election
VICTORYMESSAGE:
Happens when I have won this election
LEADERRESPONSE:
Happens when I am the leader and I have to tell others that I am alive
CLEARMESSAGE:
  Happens when I am the leader and my button has been pressed
INFECTIONMESSAGE:
Happens when I am the non-leader and my button has been pressed

## Slide 9
For each Arduino - Timers
1000:
Period for hearing replies from other devices
3000:
Period for completing an election when I receive ACKNOWLEDGE
5000:
Period for completing an election when I receive VICTORYMESSAGE
6000:
Period for monitoring leader’s response
3000:
Period for a non-leader getting infected from normal state
4000:
period for a non-leader sending infection message to all non-leaders

## Slide 10
Set up my unique ID
Initial LEDs :
Light up three LEDs
leaderID = DeviceID
Send DISCOVERYMESSAGE
To every device
Set up
Start monitoring my response

## Slide 11
Read button state
Use 50ms time interval to debounce
Record my responses if I am the leader; or start election if I don’t hear heartbeat from leader anymore when I am not the leader
Loop
Set LEDs status according to button state as leader/non-leader
Read packets from other devices and handle them
Loop

## Slide 12
Every Time Receive A New Packet
Check if the device has already added into the device list
Receive a new packet
Ensure it is a ZB_RX_RESPONSE
inList=TRUE
Add this device into device list
Continue
FALSE
TRUE

## Slide 13
Read packet and receive DISCOVERYMESSAGE
Get Remote ID
Receive the packet we want
LeaderID = remote ID
leaderID < my DeviceID
Begin Election
TRUE
TRUE
FALSE
Ask for the correct message to be sent again
Discovery
FALSE

## Slide 14
Read Pin Button
Clear Infection
Present State=Last State
Did Press The Button & Button State Changes
TRUE
FALSE
Button State=LOW
I am the leader
Send CLEARMESSAGE
TRUE
TRUE
TRUE
FALSE
isInfected=False
isInfected=True
Break

## Slide 15
Begin Election
Function Start
Is electing now?
Electing=TRUE, Acknowledge=FALSE, countdevice=0
For all devices, is its address higher than my address?
Send ELECTIONMESSAGE to that device
TRUE
FALSE
TRUE
RETURN
FALSE

## Slide 16
I am the one who start the election?
Send ELECTIONMESSAGE
to this ID address
Use a for loop to check devices in my list
listID[i] > my DeviceID?
YES
YES
NO
NO
ELECTIONMESSAGE
(Send)

## Slide 17
Get ELECTIONMESSAGE from device A
Send ACKNOWLEDGE to device A
Device A get message ACKNOWLEDGE from that device
Acknowledeged=TRUE
Variable Acknowledged becomes TRUE only if one device is not the leader of the system, which means if we find Acknowledged is FALSE in the main loop, this device should be the leader. Then it can send VICTORYMESSAGE to every device.
ELECTIONMESSAGE
(Receive)

## Slide 18
VICTORYMESSAGE
Receive VICTORYMESSAGE
newDevice ID> My DeviceID?
LeaderID = newDevice
TRUE
FALSE
Break

## Slide 19
LEADERRESPONSE
Receive LEADERRESPONSE
newDevice ID> My DeviceID
LeaderID = newDevice
My DeviceID = LeaderID
TRUE
FALSE
FALSE
Break
TRUE

## Slide 20
INFECTIONMASSAGE
Receive INFECTIONMESSAGE
LeaderID = My Device ID?
isInfected=TRUE
FALSE
TRUE
Break

## Slide 21
Challenge
Use millis() for multitasking.
  Learning about leader election algorithms.
  Set up Xbee API firmware.
  Election according to address.
Optimize delay.