## Slide 1: CHALLENGE 7 Infectious Swarm
Group 3
Aoshuang wang, lan yao, yixuan huang, lan luo

## Slide 2
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
Challenge 1 | Presenter |  |  | 
Challenge 2 |  |  | Presenter | 
Challenge 3 |  | Presenter |  | 
Challenge 4 |  |  |  | Presenter
Challenge 5 | Presenter |  |  | 
Challenge 6 |  |  | Presenter | 
Challenge 7 |  | Presenter |  | 
Challenge 8 |  |  |  | 

## Slide 3
 | Lan Yao | Aoshuang Wang | Yixuan Huang | Lan Luo
 | Program Writing | Program Writing &Debugging | Hardware Connection | Program Writing &Debugging

## Slide 4
Pressing the button with either start an infection or clear an infection depending on being a leader or a non-leader .
One leader is elected on startup. A new leader is elected if an existing leader disappears.
While infected, each device will send out infection messages to other connected devices.
A clear infection message has priority over infection message.

## Slide 5
Blue : Leader
Red : Infected
Green : uninfected

## Slide 6
For each Arduino
We tag every Arduino(XBee) with its serial address, which is unique to every Xbee.
Maintain a list of addresses of XBees that it can successfully hear from.
Whenever we add a few more new Xbees into the network, the election system can handle it by adding the address of new Xbees to the tail of the list.

## Slide 7
For each Arduino - Messages in payload includes :
Discovery :
Happens when a device is just set up/join the network at the first time
Acknowledge :
Happens when my device received a message of “begin election” from other devices
Election :
Happens when I am the one who starts the election
Victory :
Happens when I have won this election
Heartbeat :
Happens when I am the leader and I have to tell others that I am alive
Clear :
  Happens when I am the leader and my button has been pressed
Infection :
Happens when I am the non-leader and my button has been pressed

## Slide 8
For each Arduino - Timers

## Slide 9
Start
Setup
Get My Address
Initial LED
leaderAddress=Myaddress
SendMessage: MSG_DISCOVERY
Diagram

## Slide 10
Read Pin Botton
CLEAR INFECTION:
Present State=Last State
Did Press The Botton&Botton State Changes
TRUE
FALSE
Botton State=LOW
I am the leader
SendMessage: MSG_CLEAR
TRUE
TRUE
TRUE
FALSE
isInfected=False
isInfected=True
Break

## Slide 11
Discovery:
Read Packet(MSG_DISCOVERY)
Get Remote Address
Receive the packet we want
Leader Address=Remote Address
Leader Address<My Address
Begin Election
TRUE
TRUE
FALSE
Ask for the correct message to be sent again

## Slide 12
Every Time Receive A New Packet:
Check if the device has already added into the device list
Receive a new packet
inList=FALSE
inList=TRUE
Add this device into device list
Continue
FALSE
TRUE

## Slide 13
Begin Election:
Function Start
Is electing now?
IsElecting=TRUE, isAcknowledge=FALSE, countdevice=0
For all devices, is its address bigger than my address?
SendMessage: MSG_ELECTION to that device
TRUE
FALSE

## Slide 14
MSG_ELECTION
Get message(MSG_ELECTION) from device A
SendMessage:MSG_ACK to device A
Device A get message(MSG_ACK) from that device
IsAcknowledege=TRUE
Variable isAcknowledge becomes TRUE only if one device is not the leader of the system, which means if we find isAcknowledge is FALSE in the main loop, this device should be the leader. Then it can send message MSG_VICTORY to every device.

## Slide 15
MSG_VICTORY
Receive MSG_VICTORY
Remote Address> My Address?
Leader Address=Remote Address
MSG_HEARTBEAT
Receive MSG_HEARTBEAT
Remote Address > My Address
Leader Address=Remote Address
TRUE
FALSE
Break
My Address=Leader Address
TRUE
TRUE
FALSE
FALSE
Break

## Slide 16
MSG_INFECTION
Receive MSG_INFECTION
Leader Address = My Address?
isInfected=TRUE
FALSE
TRUE
Break

## Slide 17
Challenge
Use millis() for multitasking.
  Learning about leader election algorithms.
  Set up Xbee API firmware.
  Election according to address.
Optimize delay.